## Slide 1: Electric Machine Design Course
Stator Laminations & Core Design Studies
Lecture # 12

## Slide 2: Lamination cross section proportions
AC Induction:
Assume air gap circumference flux = 1.0 Tesla
All stator teeth carry total air-gap flux
Low pole numbers, max O.C. tooth flux = 1.7 T
High pole numbers, max O.C. tooth flux density = 1.4 T
Yoke flux based upon 0.5 pole flux, Max = 1.4 T
Reluctance Synchronous:
Assume air gap circumference flux = 1.0 Tesla
Stator teeth carry ~ 2/3 air-gap flux
Low pole numbers, max O.C. tooth flux = 1.7 T
High pole numbers, max O.C. tooth flux density = 1.4 T
Yoke flux based upon 0.5 pole flux, Max = 1.4 T
SPM or IPM Brushless:
Determine air gap flux/pole from magnet design
Stator teeth over rotor pole span carry rotor pole flux
Low pole numbers, max O.C. tooth flux = 1.7 T
High pole numbers, max O.C. tooth flux density = 1.4 T
Yoke flux based upon 0.5 pole flux, Max = 1.4 T

## Slide 5: Punched core laminations
Rotor cores punched from stator ID in progressive die reduces material cost.

## Slide 6: Yoke thickness of stator or rotor
Yoke thickness varies as the number of poles vs stator
OD & rotor ID for fixed stator slot depth & rotor OD
B = average air-gap flux density
By = peak yoke flux density
D = rotor OD

## Slide 7
Flux density guidelines by two experts
Max flux density in stator yoke & teeth for ACM & RSM
For open circuit PMSM machines, 1.2T/1.4T in yoke &
1.4T/1.6T in teeth for max flux density. (JRH)
Position | Typical flux density range (Say) | Maximum flux density (Lipo)
Airgap Bg | 0.65 – 0.82 T (ave.) | 
Stator yoke | 1.1 – 1.45 T (peak) | 1.7 T
Stator teeth | 1.4 – 1.7 T | 2.1 T
Rotor yoke | 1.2 T | 1.7 T
Rotor teeth | 1.5 – 1.8 T | 2.2 T

## Slide 8: Air-Gap correction factor (Carter Coefficient)

## Slide 9: Rotor & Stator Laminations
Magnetic circuit dimensions of magnetic circuit optimized for
flux densities

## Slide 10: Toyota Camry & Lexus stator lams

## Slide 11: Stacked & insulated stator cores

## Slide 12: Laminated stator cores

## Slide 13: Stator cores stacked from thin laminations

## Slide 14: Segmented stator design using either laminated stacked teeth or Sintered teeth.

## Slide 15
Skewed rotor cores for AC motors
Mitsui High-tec
Die interlocking principle

## Slide 16: Large Turbo Generator Cores
Notice- Finger Plates on core end to prevent lamination vibration

## Slide 17: Stator cores for rail traction motors
End turn supports

## Slide 18: Finger –Vent Plates
Finger Plates on
core ends prevent
lamination vibration
Vent plates in between axial groups of laminations
Fabricated by stamping and spot-welding

## Slide 19: Sintered magnetic motor cores

## Slide 20: Unusual laminated machine cores
Stator/Rotor lam for PMSM-IPM
Slinky stator core
Strip-wrap-up
Stator core
Axial flux stator
pole assembly

## Slide 21: Title

## Slide 22: Title