## Slide 1: Electric Machine Design Course
Stator Phase Circuits & Coil Design, Part 2
Lecture # 15

## Slide 2: Phase coil design guidelines
Select wye or delta phase connections. Can be series
or parallel & only wye connections require neutrals.
Select phase coil locations (Full pitch or short pitch) for highest winding distribution factor. (Unity is best)
Select number of turns per coil
Based upon required (NI) & voltage for IMs & RSMs
Based upon desired Ke for SPM & IPM motors
Select initial wire gage for about 40% bare copper to slot
area lot fill (for either single layer or multiple layer winding)
Calculate coil resistance from mean turn length times number of turns times wire resistance/inch or meter.

## Slide 3: More stator phase coil guidelines
Strands in hand of smaller gage are more flexible
Litz wire might be required for high frequency machines
Determine end turn configuration (blocking & lacing)
Select magnet wire Pig-Tails, or attach lead wires or terminal stud egress for inverter connections.
VIP or encapsulate stator to retain conductors from vibrating and to improve thermal conductivity
Large machines require end turn support against vibration
(See lecture # 13 for coil insulation topics)14

## Slide 4: Current distribution imbalance in phase conductors
New England Wire
Ohm’s law describes DC resistance where current flow is equally distributed within a conductor.
Time-varying currents induce magnetic fields that redistribute the current density in the conductors. (Most troublesome above 1KHz)
Skin effect losses & Proximity effect losses
Skin Effect:
Current flow on conductor circumference caused by increased inductive wire reactance forcing current concentration on outer surface of wire.
Skin depth =
Proximity Effect:
Conductor current density is influenced by adjacent conductors which reduces useful conductor cross section & increases AC impedance.

## Slide 5
Effect of coil or conductor inductance
vs. conductor locations within slots
Conductors are either parallel strands per
turn or turns per coil
in each slot.
Equal current sharing in each parallel conductor is very important
Else very high impedance loss results

## Slide 6: Skin effects of electrical conductors
Multiple twisted strands/turn increase effective copper area
Litz wire solution to reduce skin effect AC impedances
Certain high frequencies limit current penetration to outer skin of conductors

## Slide 7: Proximity AC loss reduction methods
Litz wire can be used with limitations
Is not effective for multiple strands/turn of Litz wire
Use of Roebel form wound coils that transposes all parallel path conductors per turn to occupy all conductor positions in each slot
For random wound coils, groups of parallel strands per turn can be transposed into different slots in the same phase, so as to have each group occupy all slot locations in each phase.
(Details of this practice left to creative machine designers)

## Slide 8: Proximity effect on phase conductors
Adjacent conductors in transformer
Blue area = high current density
White area = low current density
Conductors in PM motor slot
Blue area = high current density
Red area = low current density

## Slide 9: Parallel path conductors transposition using Roebel Coils
Transposition of parallel conductors to all slot positions for equal currents in each conductor
Coils used for large machines using rectangular wire

## Slide 10: Phase coil transposition between slots for random wound coils
Example of single layer & 2 coils/phase/pole
Four layers per slot.
Each conductor group occupies each layer in the (8) slots per phase.
Other similar combinations are possible

## Slide 11: Winding distribution vs. poles (Ratio of span of phase coils to rotor pole span)
Winding distribution factor less than unity reduces the effective turns/coil for flux linkage & resulting torque
Typically full pitch coil spans for integral slot windings result in unity winding distribution factors.
  Example: 8 poles & 12 slots (wound 1-2) yields a 86.6 % winding factor of 0.866.
  Another example: 4 poles & 12 slots with full pitch coils (wound 1-4) = 100% winding factor or 1.0.

## Slide 12: Concepts for phase coil layout procedures
Once the pole and slot number have been selected, select slots for coils/phase
(see lecture # 10 for determination of balanced slot & pole combinations)
Very little published papers or articles on this topic
Some configurations such as integral slot winding are somewhat obvious.
Most fractional slot combinations are not obvious & perhaps are “trade secrets”
Many combinations allow multiple coils slot placement options
Example (3) phases, 12 stator poles & 10 rotor poles
There are (7) different balanced winding pattern possibilities
The one with the highest winding distribution factor is preferred.
How do we come up with these winding patterns??

## Slide 13
Stator winding layout process using winding phasor method
This method has been promoted by Professor K. Reichert from Switzerland and has been taught around the world by many professors including Prof. Ing. Valéria Hrabovcová of the University of Zilina in the Slovak Republic. I am indebted to her work and teaching me to understand this technique which I am pleased to pass along in this lecture because there is very little published on this important topic.
This phasor method is based upon an important fundamental principles of rotating magnetic fields inside the stator in the air-gap cylinder between the rotor and stator.
Two pole rotor
Three phase 120 deg.
distributed stator windings
Three sinusoidal currents shifted 120 deg. apart

## Slide 14
Winding phasor method continued
The pole and phase windings must be linked like the diagram on the previous slide so we must determine the proper coil location for each phase to accomplish that proper linkage.
We must start with some term definitions used to express the important relationships used to determine the coil placements in a phasor diagram
where Y is the span or each coil. If the span is full pitch and is identical to the pole pitch.

## Slide 15
Winding phasor method continued
Using these relationships we can create a winding phasor diagram and determine the phase coil locations.
We first need the phasor diagram, along with a stator cross section with the slots numbered and we can create the slot list for the coil placements for each phase. The linear winding diagram can also be determined from this data.

## Slide 16
Winding phasor method continued
Example of a two pole (p = 2) three phase stator (m=3), cross section on the left and with the stator phasor diagram on the right. m = 3, Q = 12, q = 2,

## Slide 17
Winding phasor method continued
The resulting phase voltage diagrams spaced 120 degrees apart

## Slide 18
Winding phasor method continued
Two possible ways each phase can be inserted
Left: lap winding, all coils same span
Right: concentric winding, coil spans are not identical.
A slot list for coil locations can be easily generated from this layout of coils and numbered slots. It is often convenient to super-impose scaled pol rectangles over these slots to check the direction of current paths vs. polarities

## Slide 19
Slot-side-voltage-start method continued
K.Reichart &
J. Steinbrink

## Slide 20
Slot-side-voltage-star method
K.Reichart &
J. Steinbrink

## Slide 21
Slot locations or coil placements
12 slots
10m poles
30 degree slots
36 degree poles
Single layer winding with
2 coil/phase
Dual layer winding with
4 coil/phase