## Slide 1: Electric Machine Design Course
Introduction to Poly-Phase Induction Machines
Lecture # 16

## Slide 2: Most elegant electric motor ever invented!*
An induction or (“Asynchronous” , without synchronism) is a type of an electric machine where AC electric power is directly supplied to the stator phase windings only with no electrical connections to the rotor.
Power enters the rotor by means of electro-magnetic induction, rather than direct connection to an external supply through slip rings.
(Wound field types can and do exist powered through slip rings.)
Even though the rotor speed is not synchronized to the rotating stator field, (retarded by the “slip”), the AC induction machine constantly attempts to achieve synchronism. Therefor its speed is controlled by the AC applied frequency and its torque is controlled by slip and is effected by the voltage.
*JR Hendershot
(Almost magical)

## Slide 3: Introduction to design of AC Induction machines for flux vector control
Most existing induction machines were designed for constant Volts & Hz as powered from the grid (60Hz in USA & 50Hz in most other countries)
Motor torques produced in air gap from flux linkage from the two magnetic fields in the smooth surfaced rotor and stator
Voltage and current is supplied from the power source to only the stator
Rotor current is induced into the rotor conductors, (cage or wound)
Stator current consists of two vector components, one for magnetizing the magnetic circuit and the second for producing torque.
The AC machine design details discussed herein pertains to inverter driven machines with separate current control of the two vectors.
The principle difference between grid & inverter powered AC machines is in the rotor bar configuration, materials used and the rotor design proportions of steel and conductors.

## Slide 4: Introduction to design of AC Induction machines for flux vector control, cont.
Most common rotor winding is a single shorted turn with several parallel paths.
Most common rotor conductor has been die cast aluminum (low cost)
Grid machines @ fixed voltage and frequency require high rotor resistance for starting machine against large loads.
Inverter driven AC machines require low resistance rotor conductors
Standard NEMA & IEC AC induction machines not optimized for flux vector control of two current vectors.
AC Induction machines under 1200 Nm are optimized at 4 poles max.
Reduction in power factor and efficiency results by increasing poles
Rotor cooling of Ohmic rotor losses most limiting issue with AC Induction

## Slide 5: Example of Large AC Induction Machine
Siemens

## Slide 6
Mechanical Configuration & details of a
high performance AC induction machine

## Slide 7: AC Induction machine (IM) performance range
Fixed voltage & frequency

## Slide 8: Stator & Rotor cut-a-way for AC induction motor
E & A
Reliance
A look at the components of AC Induction machines
Rotor
Stator
Mod 16 Copyright: JR Hendershot 2012
Stator for AC Induction Motor

## Slide 9: NEMA type A, B, C & D, rotor laminations
A B
C D
NEMA type A & B rotor punching's only suitable rotor types for inverter
fed AC machines
Rotor bar shape optimization grid powered AC machines based upon the starting
torque requirements
Stator designs have been much the same for most
IM machines. The main differences lie with the rotor designs. The same
is true for inverter fed OMs
(Best option is to design brand new rotor punching for high performance IM with FIO control)

## Slide 10: Original torque vs. speed curves with constant grid voltage & frequency
(Speed vs. Torque for grid powered machines & Torque vs. Speed for inverter controlled machines)

## Slide 11: Caged rotors for AC Induction machines

## Slide 12: Cross section details of Slip Ring IM
Large versions used for Wind Turbine generators (MW size ranges)

## Slide 13: Wound rotor AC Induction machines
Rotor wound with three phase windings connected to three slip rings and brush assemblies
More expensive than caged rotors
Lower slot fills than caged rotors
Used in the past for lifting heavy loads requiring high starting torques
Used for wind turbine generators
Torque vs speed vs rotor resistance

## Slide 14: Wound rotor AC machine used as doubly fed generator
Popular wind turbine generator

## Slide 15: 3-Phase wound rotor with slip rings

## Slide 16: Equivalent Circuit of the stator
AC motor phase circuit is identical to the
primary winding of a common transformer

## Slide 17: Equivalent Circuit of the rotor
AC motor rotor cage circuit is identical to the secondary winding of a common transformer
(Unless AC rotor is three phase wound, all rotor cages
are equivalent to a single turn secondary)

## Slide 18: Complete equivalent circuit
All motor parameters can be measured and output performance can be calculated including:
Torque vs. Speed plot
Current vs Speed
Power Factor & Efficiency
Magnetizing current
See lectures 17 & 18
for more details

## Slide 19: Speed vs. Torque plots (grid powered)

## Slide 20: AC motor T vs. S @ different voltages & frequencies
Frequency varies RPM
Voltage varies slip & breakdown torque
Four pole AC induction motor
Torque vs. speed at fixed inputs

## Slide 21: Title

## Slide 22: Title