## Slide 1: Electric Machine Design Course
Poly-Phase Induction Machine Theory
Lecture # 17

## Slide 2: Basic principles in simple terms
Stator phase windings (usually (3) phases) supplied with AC voltages at some frequency
A sinusoidal rotating field results in stator and rotor
The rotor rotates slower than the field causing current to flow
which produced torque form the flux linkage of the rotor and stator
All performance depends upon the “slip” (stator field speed vs. rotor speed) for grid powered motors
Grid powered , no slip control except by applied load.
Inverter fed control both the magnetizing flux and the torque related current so the slip is not directly involved
Power factor is a function of the magnetizing & rotor currents

## Slide 3: Asynchronous nature of AC Induction machine
An AC Induction machine is sort of a synchronous machine “wan-a-be”
It runs at a speed less than stator frequency (result is called “slip”)
The magnetic field of the rotor is induced by the difference in frequencies between the stationary winding (stator phase windings rotating at line or inverter frequency) and the rotor (rotating at the slip frequency).
Therefore the shaft speed of an AC Induction or asynchronous motor is controlled by the stator phase frequency with slight variations caused but the rotor slip frequency.
Without separate magnetizing current control the rotor current varies with slip and load resulting in less than optimum torque vs. speed relationship

## Slide 4: Rotating Field of Induction Machines
Balanced three phase stator windings are mechanically displaced 120 degrees from each other, fed by a balanced three phase AC power source. (Grid or Inverter)
A rotating magnetic field with constant magnitude is produced, rotating with a speed in accordance with:
Where:
fe= supply frequency
2p = poles
nsync = synchronous RPM

## Slide 5: IM Rotating Field Plots
A B C

## Slide 6: Basic operation of AC Induction machines (Most technically elegant of all machines)
Consider a simple transformer
Square frame of iron
Wound with primary
Wound with secondary
Voltage applied primary, induces a voltage in secondary (either can be primary)
Voltage proportional to turns ratio

## Slide 7: Basic operation of AC Induction machines (Most technically elegant of all machines)
Cut iron core frame into two halves
Mount one half in bearings to facilitate rotation
Short the secondary winding or connect to external power source via slip rings
Apply AC voltage across primary
AC voltage is induced into secondary as before as flux crosses small air gaps.
With proper mechanical configuration of secondary part as a rotor in bearings and adding three phases of primary windings in a stator forces created in the air gap creates torque on the shaft.

## Slide 8
Torque production in Induction Machine
The understanding of the magnetic field that cuts the rotor windings & produces an induced voltage in the cage (which is short circuited) is assumed.
The resulting rotor current form the induced voltage produces the second magnetic field.
A torque on the shaft is produced by the linkage of those two fields.
T = induced shaft torque
BR = Rotor flux density
BS = stator flux density

## Slide 9
Speed performance of Induction Machine
  An IM rotor cannot run by itself at the synchronous speed, or at the same speed as the rotating stator field BS.
  Otherwise the rotor would appear stationary to the BS and it would not cut the rotor conductors so zero current would result with zero torque.
  When rotor speed falls below synchronous speed BS cuts the rotor conductors and produces torque.
  Result is rotor always runs at speed less than synchronous speed.
  The different in these speeds we know as the SLIP

## Slide 10: Synchronous speed, actual speed and slip
Synchronous speed RPM = (number poles)
For inverter control the more useful form:
Since the rotor rpm is less than the stator rotating field, the rotor
is said to “slip”.
Therefore slip can be expressed as:
Slip,
For motoring, slip is defined as positive,
For generating, slip is defined as negative

## Slide 11
Induction motor speed control
Speed of IM is controlled by frequency so except for slight reduction from rotor slip form stator rotating field speed the speeds vs frequency and number of poles are shown:
When IM power source was limited 50 or 60Hz grid AC, the high slip rotors bar designs permitted some speed adjustment even at fixed frequencies.
(This practice was never a good choice & now VFDs offer a much better solution allowing speeds beyond base speeds (Grid frequency speeds)

## Slide 12: Speed vs. torque curves controlled from constant V/Hz variable speed VSD inverter
Prof. TJE Miller
Fan

## Slide 13
Robert Repas, Microchip
AC Induction machine can be morphed
into a variable speed DC machine
NEMA type A & B IMs powered with inverters that control both voltage and frequency can operate from about 5 Hz up to base speed and usually at least two times beyond base speed.
Low speed peak torque is not available with these drives

## Slide 14
Flux vector control (Sometimes called field oriented control) improves IM performance even more
Two control loops are maintained at the same time, rpm & flux.
Tight Speed Regulation - 0.05% steady state error
Direct Torque Regulation – torque control from 0 to 100% torque
Control at Zero Speed – generate 300% peak torque applications
High Dynamic Response - 15 Hz response for rapid load changes
IMs driven with field oriented inverters require proper rotor designs for low resistance and frequently extreme cooling capabilities are design necessities to compete with IPMs for traction drives.

## Slide 15: IM operation envelope (motor & inverter)
Siemens
Desired performance must be contained inside envelope of family of T vs. f
curves
Note: Torque vs speed plot has been corrected
Each plot is at
fixed voltage & frequency