## Slide 1: Electric Machine Design Course
PM Synchronous Design Theory,
SPM & IPM Rotor Types
Lecture # 28

## Slide 2: Introduction for PMDC (PMDC & PMAC are the same motor type)
PMDC, BLDC or Brushless DC (Permanent magnet brushless DC motors):
- Inner, outer or axial SPM rotors (surface permanent magnets)
- Back emf seldom sinusoidal, usually sort of flat-topped
- Magnet configuration can be arc shaped or bread-loaf shaped
- Driven with “6-sep” drive, 120 deg. E commutation
“Unipolar” drive with (3) transistors, (1) phase produces torque
1/3 of stator copper utilized for producing torque & power
“Bipolar” drive with (6) transistors, (2) phases produce torque
2/3 of stator copper utilized for producing torque & power
- Stator designs typically utilize phase coils placed around single teeth
- Commutation requires shaft angle sensors or sensorless feedback
- Speed (rpm) is proportional to DC rail voltage

## Slide 3: Introduction for PMAC or PMSM (PMDC & PMAC are the same motor type)
PMAC, PMSM (Permanent magnet synchronous motor):
- Inner SPM or IPM rotors (surface or internal magnets)
- Sinusoidal back emf is desired with minimum harmonic content
- Surface magnet configuration can be arc shaped or bread-loaf shaped
- Internal magnet shapes usually simple rectangular blocks
- Driven with hysteresis current control, 180 deg. E commutation
With (6) transistor drive, all (3) phases produces torque
100% of stator copper utilized for producing torque & power
Requires shaft pole or position feedback, censored or sensorless
- Field oriented current control Id & Iq
(6) transistor bridge allows all three phases to produce shaft torque
Requires censored or measured Ld & Lq commutation
- Stator designs typically designed to facilitate sine shaped back emf
One or more slots (& coils) per pole per phase
Skew or rotor or stator or magnet pole shaping to vary air gap

## Slide 4: Back EMF comparison
Ideal Sine back EMF Ideal trapezoidal back EMF

## Slide 5: Circuit Voltage Equations
R = Resistance
L = Inductance
v = Terminal voltage
e = Induced voltage
i = Current
Φ = Flux
Ψ = Flux-Linkage
Following equations are true with constant phase inductance
It is not necessary to use these equations for initial design purposes.
A simple back EMF equation can be used for sizing the design for effective turns
FEA analysis is used for final machine design analysis

## Slide 6: Voltage & Torque relationship for PM Brushless machines

## Slide 7
Useful flux linkage equation for initial design
The PM rotor makes turns/coil calculation estimates easy
Assume Ke ~ Kt and then use the following relationship:
Z = total number of active conductors
p = number of poles
Φ = active air gap flux/pole
Assumes one parallel current path
V-sec/Rad ~ Nm/amp

## Slide 8: PM gap flux using soft iron pole concentrators

## Slide 9: IPM components
Shin-Etsu

## Slide 10: (8) Pole IPM AC synchronous motor motor
Toyota (2004) Prius
(48) Slots, (8) poles
(2) Magnets/pole
“V” shaped
Salient soft
iron poles
between
magnet
poles.
Td from magnets
Tq from salient poles

## Slide 11: IPM torque components

## Slide 12: IPM Equivalent Circuits
d-axis equivalent circuit
q-axis equivalent circuit

## Slide 13: Air-Gap flux vs magnet grade

## Slide 14: Torque and voltage relationship for brushless permanent-magnet machines
Kt = torque constant & Ke = voltage constant
For a PM brushed servo motors, Kt = Ke (SI units, Nm/A = V/rad/sec)
For a PM brushless Kt can be equal to Ke if the voltage term is properly defined (peak, mean or rms). (See chapter 8, page 405 Design of Brushless Permanent-Magnet Machines ISBN 978098068708)
The stator of a PM brushless machine usually has three phases or more, such as six, if a dual inverter bridge is used to share current.
Phase or line-line output voltage shapes are either square wave or sine wave or anything in between depending the nature of the flux linkage
due to magnet pole arc, slot/pole ratio winding pitch & skew.

## Slide 15
Peak Motor Voltage Constant Ke [Vs/rad]
Peak flux linkage per phase
This becomes the average phase EMF during 120 deg. rotation
For L-L EMF there are two phase in series and taking into account that each phase coil has two sides which are linked by the flux the equation for the peak Ke or back EMF constant is:
[Vs/rad]
The above equation is for wye connected (6) step machines. If the phase windings are connected in delta, the 2/3 factor above
is replaced by 1/3. (See page 180 in ISBN 978-09840687-0-8)

## Slide 16: Peak Motor Torque Constant Kt [Nm/A]
For PMDC motors Kt (Nm/A) = Ke (Vs/Rad)
This does not hold true for PMAC synchronous brushless machines because of the number of phases and the wide variety of back EMF shapes. (As shown on a previous slide)
Assuming close to equal relationship is very useful for first approximations for the design process but frequently, multiplying line current times the Kt will not yield torque values equal to measured values.
See chapter # 8 in ISBN 978-0-9840687-0-8 for a detailed and rigorous analysis of this topic including comparison charts on page # 422.

## Slide 17
Permanent-Magnet Synchronous Generators
Any PM brushless machine can be operated as a generator
The machine can have surface rotor magnets of imbedded magnets
The power flow from motoring to generating is reversed
A prime mover (engine, turbine or other) supplies driving torque
A back EMF proportional to rpm is produces from line to line.
The output voltages from each line to line lead can be rectified using
a simple diode bridge or an active transistor rectifier circuit.
Voltage regulation via prime mover speed control is seldom used
A down chopper is used to regulate Voltage for diode rectification
The active transistor bridge boosts the voltage for desired regulation
Mod 28 Copyright: JR Hendershot 2012

## Slide 18
Permanent-Magnet Synchronous Generator Theory
Load types: Open Circuit, Short Circuit, Infinite Bus (grid), Diode Rectifier, passive Impedance & Active Rectifier (transistors)
For Diode rectifier with down chopper for regulation the EMF is designed to be 25% to 50% higher the the regulated DC voltage.
For active transistor rectification-voltage regulation, the EMF is designed to be 25% to 50% lower than the regulated DC voltage.
(sometimes known as a boost regulator)
SPM generators exhibit very little voltage drop with load.
IPM generators can exhibit considerable voltage drop with load
PM motors generate if commutation is 180 deg from motoring
Mod 28 Copyright: JR Hendershot 2012

## Slide 19
Permanent-Magnet Synchronous Generator
Regulation with Diode Rectification
Direct Inductive-Resistive load or
DC output regulated with Transistor type Down-Chopper
LOAD
V
I
Mod 28 Copyright: JR Hendershot 2012

## Slide 20
Permanent-Magnet Synchronous Generator
Active Transistor Rectifier-Regulation
Mod 28 Copyright: JR Hendershot 2012

## Slide 21
PMG load P.F. & regulation
PMG to Infinite Bus (Wind turbine)
Voltage regulation curves with lagging P.F.
For a more rigorous discussion of PMG performance connected to different loads
see chapter 9 in ISBN 978-0-9840687-0-8
Mod 28 Copyright: JR Hendershot 2012

## Slide 22: Torque for square wave driven brushless motor
DR. TJE MILLER

## Slide 23: Title

## Slide 24: Title

## Slide 25: Title

## Slide 26: Title

## Slide 27: Title