## Slide 1: Electric Machine Design Course
Basic Electric Motor & Generator
Operational Theory
Lecture # 2

## Slide 2: Electric motor Genealogy chart
SMMA

## Slide 3: Electric Machine Cross Sections
Courtesy
TJE MILLER
a
b
c
d
e
f
g
h
Type f is an example of a double salient pole machine
Types b & h are single salient pole machines
Types a, c, d, e, f & g are non-salient pole machines
This design class is limited to the study of machines that use similar stators with the same laminations & phase windings. These are type b, c, e, g & h.

## Slide 4: Motoring & Generating Operational modes (Known as 4 quadrant operation)
- Torque +Torque
+ Speed + Speed
Torque + Torque
Speed - Speed

## Slide 5: Motoring & Generating Operation (Known as 4 quadrant operation)

## Slide 6: Example of two quadrant motor operation (Ball screw, timing belt or rack and pinion geared)
Lowest power required when times are each 1/3
Area under motion profile = motor shaft angle
Quad 1
Quad 2
+ Torque -Torque
+ RPM + RPM

## Slide 7: Introduction to basic electric motor theory
Pre-requisite technical understanding:
- First Course: Electric Machines & Drives *
- Maxwell equations for E & B field relationships
- Biot-Savart’s Law for forces on a current wire loop
- Lorentz forces from a magnetic field on a conductor
- Ampere’s Law to calculate the magnetic circuit
- Faraday’s law describes how a voltage is generated
* By Prof. Ned Mohan, Wiley2012, ISBN 978-1-118-07481-7

## Slide 8: Machine control and power source
The AC or DC power source to the inverter, converter or controller can be either from the grid or from batteries
The motor types for this series of lectures are limited to motors powered by inverters or converters & controllers.
Electric machine design techniques and strategies for grid powered machines is not covered in these lectures.

## Slide 9: General concepts of electric machines
Flux linkages between stator & rotor across air gap create or require tangential forces (resulting in torque on or from shaft) for motoring or generating.
All machines require magnetization of rotor-stator motor magnetic circuit creating circuit paths though the poles at the air gap.
- Permanent, magnets can provide magnetization - Phase or armature windings can create field flux
- Salient pole rotors close magnetic circuit paths

## Slide 10: Tangential air-gap forces producing shaft torques
PM DC commutated motor example

## Slide 11: PM Rotor with Slotted vs. Slotless stator
Magnet
Air Gap

## Slide 12: Basic operation of AC Induction machines (Most technically elegant of all machines)
Consider a simple transformer
Square frame of iron
Wound with primary
Wound with secondary
Voltage applied primary, induces a voltage in secondary (either can be primary)
Voltage in the secondary winding is proportional to turns ratio

## Slide 13: Basic operation of AC Induction machines (Most technically elegant of all machines)
Cut iron core frame into two halves
Mount one half in bearings to facilitate rotation
Short the secondary winding or connect to external power source via slip rings
Apply AC voltage across primary
AC voltage is induced into secondary as before as flux crosses small air gaps.
With proper mechanical configuration of secondary part as a rotor in bearings and adding three phases of primary windings in a stator forces created in the air gap creates torque on the shaft.

## Slide 14: PMDC commutated vs. AC induction & PM brushless
Bodine Electric
AC Induction motor PM DC commutated PM Brushless
Used over 100 yrs. Used about 60 yrs Used about 35 yrs.
Switched Reluctance motors used about 25-30 yrs.
Reluctance Synchronous motors (old motor) used a couple of years

## Slide 15: AC Induction motor (Rotating Transformer)
SECONDARY
PRIMARY

## Slide 16: Space vector diagrams for (2) pole machines
Classic DC machine
Phase of
AC induction
motor
(1) Phase of PMSM

## Slide 17: Classic PMDC to BLDC conversion
Perhaps original cross section representations of difference between the PM DC commutated motor and the PM Brushless motor now known as a permanent magnet synchronous machine.
Taken from the ELECTRO-CRAFT HANDBOOK (organized by Erland Persson), over 80,000 copies

## Slide 18: Voltage Produced in PM Machine
Faraday’s law came first so we must first consider the
open circuit voltage generated in the phase windings.
1-A moving conductor linking the flux of a constant
magnetic field produces an induced voltage.
2-An induced voltage will be induced in a conductive
coil of a magnetic flux varies inside that coil loop.
In other words an induced voltage is always produced by rate of change of flux linkage between the magnetic poles and the phase conductors

## Slide 19: Reluctance machine concept
Ld
Lq
Note: The RSM has only a single magnetic flux source (in stator)
Torque is produced by attraction of salient rotor poles to stator poles
The level of attraction (torque) is proportional to Lq / Ld

## Slide 20
PMSM
IM

## Slide 21: Title