## Slide 1: Electric Machine Design Course
Performance Calculations for
SPM & IPM Brushless Machines
Lecture # 30

## Slide 2: Design steps prior to performance calculations
Initial sizing is completed to meet spec. requirements per Lecture #4
Includes, pole and slot selection, materials, diameter and lengths
(Based upon acceptable air-gap stress, electrical and magnetic loading)
Ke to be first estimated lower than back EMF at max operation RPM
(Typical allowance of 15% to 20% for DC voltage “head room”)
The number of active stator conductors must be initially estimated after flux per pole is estimated. (See lecture # for rotor flux determination)
(Allow for flux leakage and winding factors)
Stator conductors divided by 2 divided by number of slots = turns/coil
Wire gage is calculated to fit number of turns in each net slot area
Phase resistance and current density is initially estimated

## Slide 3: Calculate number of turns per coil
R.G. Harley and Y. Duan
Calculate number of stator turns per phase depending on previous B, D, L, supply voltage (math) and assumed flux density shape fa
Kf : form factor, typically assumed = 1
Kw1 : winding factor
f : fundamental frequency based upon poles & speed
KE: typically allows for higher for large power rating or small pole number [4
Flux per pole
Bg = 2p Φm/(πDL) to find Φm
Back EMF factor
Turns per phase

## Slide 4: Title

## Slide 5: Commutation important to performance
BLDCs & PMSMs are identified as synchronous AC machines
One could support a strong argument against this notion.
AC machine are speed controlled by frequency
These machines are is speed controlled by changing voltage.
These machines require self-synronization through shaft angle sensors such as hall switches, encoders or resolvers.
What is the relationship between the shaft angle feedback data? Commutation of inverter currents to stator phase windings
Must synchronize to rotor poles during rotation and startup
If halls switched are used, where must they be located?

## Slide 6: Hall switch placement guidelines
Conditions of hall placements:
PM brushless machines are normally bi-polar driven so there are two control events/phase required for electronic commutation.
Each hall switch has two possible states
Three phases requires 6 control events.
Two hall switches provides 22 states & three provide 23
Four control states is not enough so three halls are required
For balanced (3) phases the slot number must be factorable by (3)
The phase set coil distributions & must be 120 deg. M apart
For even slot numbers, halls are placed in line with the slot openings
For odd slot numbers, halls are placed in line with tooth center.

## Slide 7: Hall output alignment to back EMF (for CW rotation)
Each hall switch must be aligned with it’s
corresponding L-L back emf zero crossings

## Slide 8: Hall output alignment to back EMF (for CCW rotation)
Each hall switch must be aligned with it’s
corresponding L-L back emf zero crossings

## Slide 9: Determine angle hall switches are spaced apart
For (m) phases, 360/m = β (electrical angle spacing of halls
Electrical phase angle) / (hall spacing mech. angle)
β/p = hall spacing in mech. degrees
Compliment spacing of center hall can be uses but hall numbers 2 & 3 must be reversed for gate connections

## Slide 10: Open Circuit Cogging Torque
Break away torque from stall is known as cogging Torque
Cogging torque periodicity a function of number poles & slots
Magnitude dependent on magnet flux & magnetic reluctance
Optimized by selection of slots/pole & magnet pole angle
Near elimination results from either pole or stator skewing
Optimized magnet pole shape reduces cogging torque
Unequal pole spacing reducing cogging torque

## Slide 11: Cogging torque predictions as a function of rotor angle with respect to stator
There are two principle ways to predict the open circuit low speed reluctance torque (known as cogging torque) between the PM rotor
and the stator teeth due to the alignment of the slot openings
Integrate the Maxwell stress tensor within the air-gap. This requires a very complex derivation of the air-gap permeance from the slot geometry. To get at the cogging torque the radial & tangential components of the air-gap flux density are required.
The alternative is to utilize a magnetic FEA solver to calculate the air-gap flux and its components to yield a cogging plot as a function of rotor angle
Cogging is easily measured with a Torque Watch …

## Slide 12: Measuring Cogging Torques
Cogging torques can best be measures using delicate torque measuring instruments called a Torque Watch.
Easily attaches to motor shaft using included three jaw chuck
The watch type face includes a peak
torque memory pointer which can be
reset to zero after each measurement
Next slide lists the ranges available from
two suppliers:
Honeywell & Tohnichi

## Slide 13: Torque watch sizes

## Slide 14: Torque calculation guidelines for BLDCs & PMSMs
Kt (Nm/Amp) is the result of the rotor magnet flux linkage with the stator phase conductors, or 2(Turns/coil)(number of coils) = Z , or total stator conductors times possible winding factors.
Therefor torque control requires current control
Current is controlled by the drive circuits from the converter
Faraday’s law states that the rate of change of flux linkage equals
the induced voltage.
Turns x flux = ψ = Nϕ = ψM + Li
Circuit voltage equation with
constant inductance,
V = terminal voltage
R = resistance
L = inductance
e = induced voltage
i = current

## Slide 15: Torque equations for (3) phase PM machines
After a design is sized, flux/pole, number of conductors determined and assuming the ideal current waveform can be injected into the stator windings, specific alignment torque/amp calculations can be made for both squarewave & sinewave machines.
Nm/A for d axis torques (alignment torque) only, typically for SPMs
(Note: Alignment torque is a function of the magnet flux & stator current.
It is usually quite linear as long there is no effects of saturation in the circuit.)
Nm/A, Torque/Amp
(3) phase sinewave
Nm/A, Torque/Amp
(3) phase squarewave

## Slide 16: Reluctance torque
Salient pole machines like RSMs & SRMs produce torque through an attraction type flux linkage producing reluctance torque.
RSMs are designed with saliency only in the rotor.
SRMs are configured with saliency in both the stator & rotor
The reluctance of either machines is determined by the ratio of the d & q saliency, defined by inductance ratio, Ld / Lq
As increasing currents the ratio decreases as the flux density in the circuit increases.
Without saturation the reluctance torque is proportional to the applied phase current squared
RSM
SRM

## Slide 17: IPM rotor details necessary for torque calculations
IPM machines are usually designed with rotor saliency between magnet poles.
Therefore there are two torque producing components:
- Alignment torque from the rotor magnet flux linkage (d axis)
- Reluctance torque from the rotor saliency from the (q axis)
from the soft iron poles between permanent magnet poles.
d
q
Pole magnets can be multi-layered, single
slab or V slab shaped

## Slide 18: Torque equation for IPM machines
Total torque
Reluctance torque
Alignment torque
Torque plots vs. current for PMSM-IPM
Optimum phase advance angle γ
IPM rotor configured
to maximize sum of
the reluctance and
alignment torques.

## Slide 19: Title

## Slide 20: Title

## Slide 21: Title

## Slide 22: Title