## Slide 1: Electric Machine Design Course
Electric Machine Sizing
Lecture # 5

## Slide 2: Sizing of electrical machines using torque/rotor volume & gap stress
Machines are primarily sized for rated torque capability (not power).
Output torque is proportional to product of rotor volume & shear stress
Air-gap shear stress is proportional to product of air-gap electrical & magnetic loading.
Many IM & RSM machines are 4 pole so most of the rotor volume is magnetically active.
Perhaps the best sizing parameter for IMs & RSMs is TRV
Brushless or PMSM machines tend to have higher poles (8 or more)
The best sizing parameter for PMSMs is probably air gaps stress.

## Slide 3: Rating considerations for electrical machines
Dimensions of a machine depend on:
  Output torque at a specific speeds
  Air gap stress
  Air gap flux density
  Air gap current density
  Phase conductor current density
  Enclosure type, (TEFC, ODP, TEPV, TENC etc.)
  Type of cooling (Natural, air over, forced air & liquid)
  The duty cycle of the load
  The frequency of starting and stopping

## Slide 4: Rotor to stator diameter vs. number poles once the stator OD is known
Most all new design tasks of new machines begin with a known or given maximum stator core diameter.
Start the design with an assumed rotor diameter based upon the number of poles from chart below.
After machine sizing based upon the next few slides the core length is set for the final design analysis.

## Slide 5: Historical sizing method for electric machines
TRV = Torque / Rotor Volume (active)
TRV is related to air-gap shear stress
= Air-Gap shear stress
= Torque/gap radius/swept gap area
Swept gap area = D l
B
Ad

## Slide 6: Suggested TRV & gap stress sizing guidelines
10 kPa = 1.45 Psi
Prof. TJE Miller

## Slide 7: Machine Electric Loading
Current density in A/m, (Ad ) in the phase conductors is a measure of the current loading and determines either the machine duty cycle or the cooling requirements.
The linear current density around the circumference of the
air-gap between the rotor and stator can also be used to
characterize the electric loading of the machine.
Prof. TJE Miller

## Slide 8: Electric loading in air gap
Gap-loading
= Total amp-conductors/gap circumference
n = number of phases, N = turns /phase
I = rms Phase current, D = air-gap diameter

## Slide 9: Typical phase conductor current densities

## Slide 10: Magnetic air gap loading
Magnetic air-gap loading analysis is sometimes used is machine sizing studies that is based upon the average flux density in the air gap.
For example is is typical to try for air gap flux densities in the range of 0.75 to 1.0 Tesla. This is a desired starting place for the design of induction machine as well as RSM and PM rotors.
To facilitate effective utilization of magnetic air gap loading for machine sizing, acceptable values must be available from measure-ments of existing machines that utilize similar methods of cooling with natural convection, forced air cooling or liquid cooling.
Prof. TJE Miller

## Slide 11: Sizing of high speed machines
Air gap stress guidelines and limitations on cooling must not be ignored
For high speed rotors, the rotor retention for stable rotor dynamics is most important consideration
Any movement of rotating components can cause unbalance leading to potential rotor failure or catastrophic contact with stator I.D.
Start first with max allowable rotor “tip speed” (m/sec) and solve for air gap diameter (Dr) and length (Lr) to achieve desired air gap stress
Tip Speed (m/sec) = (π/60) Dr (rpm)
Tip speeds 75 m/sec for high strength non-magnetic alloy sleeves & 100 m/sec and higher for pre-stressed carbon fiber sleeves

## Slide 12: Additional suggestions for IM & RSM sizing
If the specification places no limits on stator O.D. the TRV method for machine sizing can be used.
The generally accepted practice for rotor D/L proportions has the rotor diameter at 0.5 to 2 times the rotor core length.
The continuous duty current density can be reduced by either increasing the core lengths or increasing the stator OD thereby providing for deeper stator slots for more winding space.
If low inertial is a requirement then the D/L ratio determination
must be optimized based upon the inertia related related to the diameter squared and the length is directly proportional.

## Slide 13: Motor sizing the easy way or use as sanity check
Well known fact that AC induction machines have rotor Ohmic losses which results in lower continuous ratings than SR, RSM or PMSMs
(If this comment is arguable, assume all machines about the same)
Several firms including ATE in Germany sell a complete line of rotor and stator elements fully tested and rated in two classes, S1 & S3
Cooling information such as liquid are provided as well
ATE lists the dimensional details of these rotor and stators along with their speeds and output power ratings in both rating classes.
Use of these published machine rating lists provides the electrical machine designer an excellent starting place for either a new design or as a sanity check to compare with his new design.
Other motor vendors who publish similar performance data & dimensions for their motor elements are: Rueland (USA) and E und A (Switzerland)

## Slide 14: ATE motor element (4) Pole vs. KW data

## Slide 15
ATE motor element
(6) Pole vs.KW data

## Slide 16
ATE motor element
(8) Pole vs. KW data

## Slide 17: Title

## Slide 18: Title

## Slide 19: Title

## Slide 20: Title